## Slide 1: LSTM reduction of a Gas Turbine for Real-Time simulation
Ioannis Myrsinias Application Support Engineer
14/11/2023
Notes: Good morning/afternoon/evening everyone, and welcome to our webinar today. I am delighted to share with you an exciting journey that takes us from a published article through a reduced-order model, to its real-time simulation on Speedgoat.
Real-time simulations of real-world systems offer immense potential for revolutionizing hardware in the loop testing and predictive maintenance control. By utilizing accurate digital twins, these simulations can significantly reduce design and prototyping costs while expediting the production of real systems. However, the challenge lies in the limited computational resources, which can pose a barrier to the complexity of real systems that we can simulate in real-time. This is where reduced-order models play a crucial role in reducing complexity with reasonable accuracy.
Bonjour à tous, bienvenue à notre webinaire aujourd'hui. Je suis ravi de partager avec vous un voyage passionnant qui nous emmène d'un article publié à un modèle à ordre réduit, déployé pour une simulation en temps réel sur Speedgoat.
Les simulations en temps réel de systèmes physiques peuvent ouvrir la voie aux tests matériels en boucle fermée, au prototypage rapide et à la maintenance prédictive, réduisant ainsi les coûts et le temps des systèmes réels. Cependemt Les ressources de calcul limitées constituent une barrière à la complexité des systèmes physiques que nous pouvons simuler en temps réel. C'est là que les modèles à ordre réduit jouent un rôle important en réduisant la complexité avec une précision raisonnable.

## Slide 2: From a published article to real time simulation
97.5% precise
40% faster
model
reduce
compare
deploy
emulate
exhaust
Compressor turbine
Compressor
Combustion chamber
Free power turbine
Power shaft
Notes: Today our journey will take us from a published article on how to model a turboshaft engine of a helicopter, to its reduction and its real-time simulation. We will walk through each step of this workflow using MATLAB and Simulink.
Inspired by the published paper we will create an equivalent physical model in Simulink using Simscape components to model the operation of a turboshaft engine
Then We will simulate it user different scenarios to generate data.
Data of which we will use in data driven AI technics to create a reduced order model. Data driven technics are getting more and more attention since nowadays and this can be a good showcase of the capabilities and performances of LSTM recurrent networks
Then we will compare the ROM with the physical model in terms of
How precise and how performant it is
We will generate code and deploy it on a real time computer to emulate its response.
Let’s get started
Les résultats que nous avons obtenus sont vraiment remarquables : une réduction de 30% du temps de simulation et une précision quasi parfaite d'environ 98% pour notre modèle à ordre réduit.
Dis par rapport du background

## Slide 4: From a published article to real time simulation
model
reduce
compare
deploy
emulate
estimate TET, Power
exhaust
Compressor turbine
Compressor
Combustion chamber
Free power turbine
Power shaft

## Slide 5: Conclusion
All in one ecosystem
Model, Reduce, Test, Emulate
Estimate what we cannot measure
Burner exit temperature
Mechanical power
Simulate real-time
Hardware in the loop testing
New opportunities:
Predictive maintenance and control
Accelerate prototyping
Learn from the experience
Performant ~40% faster
Accurate ~2.5% relative tolerance

## Slide 6: Thank you for your attention! Do you have any questions?
Notes: What are this project’s goals

## Slide 7: DRAFT
Notes: What are this project’s goals

## Slide 8: Conclusion
All in one ecosystem
Model, Reduce, Test, Emulate
Learn from the experience
Performant ~40% faster
Accurate ~2.5% relative tolerance
Estimate what we cannot measure
Burner exit temperature
Mechanical power
Simulate real-time
Hardware in the loop testing
Predictive maintenance and control
Accelerate prototyping

## Slide 9: Real time simulations
Reduced cost
Hardware in the loop
Reduced Order Model
Real System
Emulation
Flexible design
Notes: Les simulations en temps réel de systèmes physiques peuvent ouvrir la voie aux tests matériels en boucle fermée, au prototypage rapide et à la maintenance prédictive, réduisant ainsi les coûts et le temps des systèmes réels. Cependemt Les ressources de calcul limitées constituent une barrière à la complexité des systèmes physiques que nous pouvons simuler en temps réel. C'est là que les modèles à ordre réduit jouent un rôle important en réduisant la complexité avec une précision raisonnable.

## Slide 10: Real time simulations
Reduced cost
Flexible design
Reduced Order Model
Real System
Emulation
Flexible design
Notes: Les simulations en temps réel de systèmes physiques peuvent ouvrir la voie aux tests matériels en boucle fermée, au prototypage rapide et à la maintenance prédictive, réduisant ainsi les coûts et le temps des systèmes réels. Cependemt Les ressources de calcul limitées constituent une barrière à la complexité des systèmes physiques que nous pouvons simuler en temps réel. C'est là que les modèles à ordre réduit jouent un rôle important en réduisant la complexité avec une précision raisonnable.

## Slide 11: Conclusion
Model, reduce, test, deploy and emulate in one ecosystem
Learn from the experience
Performant ~60% faster
Accurate ~2.5% relative tolerance
Estimate magnitudes difficult to measure
Simulate real-time and pave the way for
Hardware in the loop
Rapid prototyping
Predictive maintenance

## Slide 12: Conclusion
All in one ecosystem
Model, Reduce, Test, Emulate
Learn from the experience
Performant ~60% faster
Accurate ~2.5% relative tolerance
Estimate what cannot measure
Burner exit temperature
Mechanical power
Simulate real-time
Hardware in the loop
Rapid prototyping
Predictive maintenance

## Slide 13: Contents
Introduction – AIRBUS invests in AI
Model reduction for Hardware in the loop
Turboshaft Engine in Simulink
Reduced Order Model
Demonstration – Reduced order model with LSTM network
Conclusion

## Slide 14: Conclusion
Possible to learn from the experience
LSTM networks are sensitive to data quality
Increase model performance
Accurate response
Areas of attention
Data drifting
Long timeseries
OOD : out of distribution data

## Slide 15: Lessons learned
Model
Reduce
Compare
Deploy
Emulate